## Slide 1: Accelerate Reconstruction by Implementing ADMM in FPGA
University of North Dakota EE department
EECSXXX, Ray Duran
Prof Bo Liang
8/19/22

## Slide 2: Agenda
Motivation/Applications
Brief Top-Level description ADMM
Assumptions
Engines Flow Diagram
  U, X and W update(primal)
  Rk and Rdiv(primal)
  Image Update(primal)
  Rho,Ksee, and eta update(dual)
Algorithm Flow Diagram
Calculations/Speed
Resources
Device
Discussion/Conclusion

## Slide 3: Motivation
Problem: In-vivo calcium imaging with a diffuser to improve FoV and resolution tradeoffs, implemented in FPGA
Related work:
  Research at UCLA from Jason Cong
  Research at UC. Berkeley with Laura Waller
Provide imaging community with a “pluggable” core for further investigations
ADMM faster than gradient methods(FISTA and Nesterov momentum)
Lay foundational FPGA for above applications this semester

## Slide 4: Top –Level ADMM
Take original optimization problem
Split into separate minimizations
Add regularization
Augmented Lagrangian
Form dual updates to minimize with one set of engines and maximize with another: “Duality: min-max”
Allows a very optimized approach by divide and conquer

## Slide 5: Assumptions
Downscale to 512x1024
Process only Luma
8 bit( Mainstream)
Ultrascale+

## Slide 6: U update
Div
ψ
μ2
Τ
ηk
uk+1
vk

## Slide 7: X update
(C^C + u1I)^-1
FFT2
xk+1
vk
H
IFFT2/SHFT
μ1
ξk
C^b

## Slide 8: W update
Max
vk
wk+1
k
ρ
Div
μ3

## Slide 9: rk update
ηk
rk
ρk
uk+1
ξk
μ3
μ1
μ2
wk+1
xk+1
ψT
FFT2
H*
IFFT2/SHFT

## Slide 10: Rdivmat update(pre-compute)
ψtψ
Inv()
H
Rdivmat
H*
Abs
μ1
μ2
μ3

## Slide 11: Image update
vk+1
rk
FFT2
IFFT2
Rdivmat

## Slide 12: ρ update
Vk+1
ρk +1
μ2
wk+1
Z^-1

## Slide 13: ξ update
vk+1
ξk +1
FFT2
H
IFFT2/SHFT
μ1
xk+1
Z^-1

## Slide 14: η update
ψ
vk+1
μ2
ηk+1
Z^-1
uk+1

## Slide 15: ADMM Algorithm
ηk
u update
vk
ξk
x update
vk
Ctb
ρk
w update
vk
rk
FFT2
IFFT2
Rdivmat
ξupdate
ηupdate
ρupdate
ρk
vk+1
ηk
ξk
ηk ξk ρk
xk+1
uk+1
wk+1

## Slide 16: Speed/Latency Calc & Strategy
Bottlenecks FFT2/IFFT2 processing
5*(4*(2*2(156us))) = 1 frame
Fmax = 300 Mhz
156us from Ray Duran Sp,BME690
1 frame = 9.36ms
Can Run over 60Hz!

## Slide 17: Resource Estimates
 | u update | x update | w update | rx | Rdiv(pre) | image | rho | xi | eta
xpre |  | 1 |  |  |  |  |  |  | 
div | 1 |  | 1 |  |  |  |  |  | 
psiorpsiT | 1 |  |  | 1 |  |  |  |  | 1
adder | 1 | 1 | 1 | 4 | 1 |  | 1 | 2 | 2
mult |  | 3 |  | 4 | 3 | 1 | 1 | 3 | 2
fft/ifft |  | 1 |  | 1 |  | 1 |  | 1 | 
max |  |  | 1 |  |  |  |  |  | 
thresh | 1 |  |  |  |  |  |  |  | 
abs |  |  |  |  | 1 |  |  |  | 
inv |  |  |  |  | 1 |  |  |  | 
psi/psiT |  |  |  |  | 1 |  |  |  | 
Notes: Here is that medium.; A diffuser can be thought of as a kind of random matrix. So, all we would then need is for our voxels to be sparse in some domain. As we saw earlier in Professor Liang’s lecture on compressive imaging, we are saved as a random matrix multiplied by another matrix is still random. So, if we transpose our solution into a spare domain with some matrix we are still random.

## Slide 18: Resource Estimation
Divider:
FFT :
Notes: Here is that medium.; A diffuser can be thought of as a kind of random matrix. So, all we would then need is for our voxels to be sparse in some domain. As we saw earlier in Professor Liang’s lecture on compressive imaging, we are saved as a random matrix multiplied by another matrix is still random. So, if we transpose our solution into a spare domain with some matrix we are still random.

## Slide 19: Resource Estimation
 | LUTS | FF | DSP | 36KBRAM | 18KBRAM
Divider-Uupdate | 1279 | 3334 | 0 | 0 | 0
Divider -Wupdate | 1279 | 3334 | 0 | 0 | 0
FFT-Xupdate | 7568 | 13554 | 48 | 0 | 16
IFFT-Xupdate | 7568 | 13554 | 48 | 0 | 16
FFT-rx | 7568 | 13554 | 48 | 0 | 16
IFFT-rx | 7568 | 13554 | 48 | 0 | 16
FFT-image | 7568 | 13554 | 48 | 0 | 16
IFFT-image | 7568 | 13554 | 48 | 0 | 16
FFT-xi | 7568 | 13554 | 48 | 0 | 16
IFFT-xi | 7568 | 13554 | 48 | 0 | 16
Total | 63102 | 115100 | 384 | 0 | 128
Notes: Here is that medium.; A diffuser can be thought of as a kind of random matrix. So, all we would then need is for our voxels to be sparse in some domain. As we saw earlier in Professor Liang’s lecture on compressive imaging, we are saved as a random matrix multiplied by another matrix is still random. So, if we transpose our solution into a spare domain with some matrix we are still random.

## Slide 20: Resource Estimation
Div & FFT estimate 70% of resources
Notes: Here is that medium.; A diffuser can be thought of as a kind of random matrix. So, all we would then need is for our voxels to be sparse in some domain. As we saw earlier in Professor Liang’s lecture on compressive imaging, we are saved as a random matrix multiplied by another matrix is still random. So, if we transpose our solution into a spare domain with some matrix we are still random.

## Slide 21: Device
Notes: Here is that medium.; A diffuser can be thought of as a kind of random matrix. So, all we would then need is for our voxels to be sparse in some domain. As we saw earlier in Professor Liang’s lecture on compressive imaging, we are saved as a random matrix multiplied by another matrix is still random. So, if we transpose our solution into a spare domain with some matrix we are still random.

## Slide 22: Discussion/Conclusion
Tools, supplies( matlab, python,modelsim(questa), paid Xilinx(FFT)
Schedule
FFT2 core(AXI-bus)
Use as a IP for future work
Upload to github for community

## Slide 23: Partial References
N. Antipa et al., “DiffuserCam: lensless single-exposure 3D imaging single-shot,” Optica 5,1-9 (2018).
E. Bezzam, et al., “ LenslessPiCam: A Hardware and Software Platform for Lensless Compuational Imaging with a Raspberry Pi,” (2022)
Stephen Boyd, Neal Parikh, Eric Chu, Borja Peleato, and Jonathan Eckstein. Distributed optimization and statistical learning via the alternating direction method of multipliers. Found. Trends Mach. Learn., 3(1):1–122, jan 2011.
K. Monakhova et al.”Learned reconstruction for practical mask-based lensless imaging,Optica Express (2019)
https://www.xilinx.com/htmldocs/ip_docs/pru_files/div-gen.html
https://www.xilinx.com/htmldocs/ip_docs/pru_files/xfft.html